Heres the ELSA discription on how to do it, and a pic of what its like once removed.


Dash panelRemoving and installing dash panel >

04.00Warning!
Disconnect battery earth strap before working on the electrical system.Removing

Notes:

Obtain radio unit code before disconnecting battery. After connecting battery, check vehicle equipment (radio, clock, electric windows) as per Workshop manual and/or Owner's manual.

The wiring harness is secured to the dash panel by clips. The wiring harness remains in the vehicle when removing the dash panel.

Remove steering wheel

Remove centre console

Remove driver's stowage compartment

- Remove front passenger's stowage compartment

- Remove bonnet release lever

Remove Qty. 3 screws -arrows-.

Pull connectors off steering column switch.

- Take off steering column switch.

Remove Qty. 2 screws -arrows-.

- Take off upper part of instrument binnacle.

Remove Qty. 4 screws -arrows-.

- Take off lower part of instrument binnacle.

Remove Qty. 2 screws -arrows-.

Take out combi instrument.

- Unclip connector.

- Remove hexagon nuts -arrows-.

Note:

- The two hexagon nuts are visible first after removing the combi instrument.

Press in lighting switch -arrow-, turn clockwise and pull out.

- Unclip connector.

Remove bolt -arrow-.

Pull out vent on driver's side -1-.

- Pull off connector on headlight range control -2-.

Unclip treble loudspeakers on left and right-hand sides using a small screwdriver.

- Unclip connector.

- Remove Qty. 4 screws -arrows-.

Remove Qty. 2 screws -arrows-.

- Take out driver's side footwell cover.

- Remove screw -1- and unclip trim -2- on left and right.

Unclip cover cap -1- on left and right.

- Remove bolt -2- on left and right-hand sides.

- …Remove bolt -arrow- on left and right-hand sides.

Remove two screws -1-. Take off switch carrier -2-.

- Unclip connector.

Slide radio release tool 3316 into the release slots until they engage.

- Pull radio out of the dash panel using the grip rings of the release tools and disconnect connectors.

Notes:

When doing this the radio release tool 3316 must not be pushed to the side or tilted.

- To remove the release tools from the radio the locating lugs on the side of the radio must be pressed inwards.

- Pull out stowage compartment -1-.

Remove Qty. 3 screws -arrows-.

- Take out centre vent.

Remove Qty. 2 screws -1-

. Remove hexagon nut -2-.

Take out support -3-.

- Remove Qty. 2 screws -arrows-.

Note:

- The screws are visible through the elongated holes, they are set back approx. 2 cm.

Remove Qty. 3 screws -arrows-.

- Take off pollen filter maintenance flap.

Unclip pollen filter frame -1-.

Take out pollen filter -2-.

Remove hexagon nuts -3-.

- Take out pollen filter housing -4-.

- Remove Qty. 4 bolts -arrows-.

- Pull dash panel out slightly.

Note:

- The wiring harness is secured to the dash panel by clips and cable ties. The wiring harness remains in the vehicle when removing the dash panel.

Release clips, cable ties and connectors depending upon the vehicle equipment level.

- Lift out dash panel.

Installing

Install in reverse order.

Note:

- If the airbag fault warning lamp (K 75) signals a fault after assembling then the fault memory must be erased and interrogated again with fault reader V.A.G 1551